Basic-block vectorization
for graphics compilers
Robert Foss

---
About vectorization
Vectorization 101
load
load
load
load
add
add
add
add

---
About vectorization
Vectorization 101
load
load
load
load
2 x add
add
add

---
More about vectorization
Techniques
Several techniques exist
- Loop-based vectorization
- Basic-block vectorization
- Superword Level Parallelism vectorization

---
Basic-block vectorization
Control Flow Graph
Entry
Entry
Basic-block
a = 1
a += 1
if a < 9
Basic-block
Exit

---
Basic-block vectorization
Basic-block
const1 = constant <1 x u32> 0x1
const2 = constant <1 x u32> 0x2
a = add <1 x u32> a const1
b = add <1 x u32> b const2
c = add <1 x u32> a b
const3 = constant <1 x u32> 0x9
bool = icmp _ult c c3
br bool dest1 dest2
a += 1
b += 2
c = a + b
if c < 9

---
Basic-block vectorization
a
const1
b
const2
add
add
add
icmp
br

---
Basic-block vectorization
a
b
const2
const1
add
add
add
icmp

---
Basic-block vectorization
a
const1
const2
b
move
2 x add
move
add
icmp

---
Basic-block vectorization
a
const1
const2
b
move
2 x add
move
move
move
add

---
Basic-block vectorization
Alternatives
Two algorithms were implemented
- LLVM-based basic-block vectorization
- Pair-based basic-block vectorization

---
LLVM-based vectorization
Steps involved:
- Find potential pairs
- Find connections between pairs
- Pair selection
- Pair fusing
- Fixed-point iteration

---
LLVM-based vectorization
Find potential pairs
add#1, #2
add#2, #3
add#1
add#2
add#3
add#1, #3
mul#1
mul#2
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1
cmp#2
cmp#3
cmp#1, #3

---
LLVM-based vectorization
Find potential pairs
add#1, #2
add#2, #3
Steps involved:
add#1, #3
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #3

---
LLVM-based vectorization
Find potential pairs
add#1, #2
add#2, #3
Steps involved:
add#1, #3
Remove intradependent pairs
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #3

---
LLVM-based vectorization
Find potential pairs
add#1, #2
add#2, #3
Steps involved:
add#1, #3
- Remove intradependent pairs
- Remove illegal pairs
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #3

---
LLVM-based vectorization
Find pair connections
add#1, #2
add#2, #3
mul#1, #2
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #2
cmp#2, #3

---
LLVM-based vectorization
Pair selection
add#1, #2
add#2, #3
mul#1, #2
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #2
cmp#2, #3

---
LLVM-based vectorization
Pair selection
add#1, #2
add#2, #3
mul#1, #2
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #2
cmp#2, #3

---
Pair-based vectorization
Steps involved:
- Find potential pairs
- Pair selection
- Pair fusing
- Fixed-point iteration

---
Pair-based vectorization
Find potential pairs
add#1, #2
add#2, #3
add#1
add#2
add#3
add#1, #3
mul#1
mul#2
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1
cmp#2
cmp#3
cmp#1, #3

---
Pair-based vectorization
Find potential pairs
add#1, #2
add#2, #3
Steps involved:
add#1, #3
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #3

---
Pair-based vectorization
Find potential pairs
add#1, #2
add#2, #3
Steps involved:
add#1, #3
Remove intradependent pairs
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #3

---
Pair-based vectorization
Find potential pairs
add#1, #2
add#2, #3
Steps involved:
add#1, #3
- Remove intradependent pairs
- Remove illegal pairs
mul#1, #2
cmp#1, #2
cmp#2, #3
cmp#1, #3

---
Pair-based vectorization
Pair selection
add#1, #2
add#2, #3
mul#1, #2
cmp#1, #2
cmp#2, #3

---
Pair-based vectorization
Pair selection
add#1, #2
add#2, #3
mul#1, #2
cmp#1, #2
cmp#2, #3
Fuse most profitable pair

---
Pair-based vectorization
Pair selection
add#1, #2
add#2, #3
mul#1, #2
cmp#1, #2
cmp#2, #3
Fuse most profitable pair
Remove already fused operations

---
Pair-based vectorization
Pair selection
add#1, #2
add#2, #3
mul#1, #2
cmp#1, #2
cmp#2, #3
Fuse most profitable pair
Remove already fused operations
Remove intradependent pairs

---
Pair-based vectorization
Pair selection
add#1, #2
add#2, #3
mul#1, #2
cmp#1, #2
cmp#2, #3
Fuse most profitable pair
Remove already fused operations
Remove intradependent pairs
Fixed-point iteration

---
Heuristics
What? Why?
Are used to determine profitability

---
Heuristics
What? Why?
Are used to determine profitability
Avoid NP-complete problems like
Longest path / Hamiltonian path

---
Heuristics
What? Why?

---
Heuristics
Which? How?
a
const1
const2
b
move
2 x add
move
move
move
add

---
Heuristics
Which? How?
a
const1
const2
b
move
2 x add
move
No need to move data
move
move
add

---
Heuristics
Which? How?
a
const1
const2
b
move
2 x add
move
move
add

---
Heuristics
Which? How?
a
const1
const2
b
move
2 x add
move
Can often be done
for free with the
swizzle modifier
move
add

---
Heuristics
Which? How?
a
const1
const2
b
move
2 x add
move
add

---
Heuristics
Which? How?
a
const1
const2
b
Constants can be
~freely combined into
new vector constants
move
2 x add
move
add

---
Heuristics
Which? How?
a
const1, const2
b
move
2 x add
add

---
Heuristics
Which? How?
If the operation a
is the same operation
as b
a
const1, const2
b
move
2 x add
add

---
Heuristics
Which? How?
If the operation a
is the same operation
as b
a==b
const1, const2
move
2 x add
add

---
Heuristics
Which? How?
If the operation a
is the same operation
as b
a==b
const1, const2
Can often be done
for free with the
swizzle modifier
move
2 x add
add

---
Heuristics
Which? How?
a==b
const1, const2
2 x add
add

---
Results
Work Register Usage

---
Results
Work Register Usage

---
Results
Arithmetic Cycles

---
Results
Arithmetic Cycles

---
Results
Compilation Time

---
Results
Why?

---
Results
Why?
Increased register pressure

---
Results
Why?
Increased register pressure
Increased scheduling tightness

---
Results
Why?
Increased register pressure
Increased scheduling tightness
The cost of moving data around

---
Basic-block vectorization
for graphics compilers
Robert Foss